## Slide 1: Investigating instrument resolution with McStas
ISIS 2025 McStas School
PRESENTED BY Mads Bertelsen

## Slide 2: Resolution
  Two important concepts:
  Point spread function: Distribution on detector from specific q, E
    Used to build expected detector response from known q, E distribution
  Detector response: Distribution of q, E measured by part of detector (pixel, time)
    Used to build up map of q, E measured from detector response
  Depends on almost all aspects of instrument:
    Source size/time structure, optics, sample size/shape, detector, …
What do we mean by instrument resolution?

## Slide 3: Resolution
  Spot_sample (in Contrib, by Garrett Granroth)
  Number of spots in q, E
  Probes the point spread function for all these spots in one simulation
Tools for point spread function

## Slide 4: Resolution
  Continuous measurements Res_sample.comp / Res_monitor.comp
Tools for detector response
Start of instrument
Res_sample
Res_monitor
Sample sends rays towards monitor.
Selects random final energy in given interval.
Sample records q, E for each event
Monitor histograms those that reach it

## Slide 5: Resolution
  Terminal tool: mcresplot
Tools for detector response

## Slide 6: Resolution
  Time of flight measurements TOFRes_sample.comp / TOFRes_monitor.comp
Tools for detector response TOF case
Start of instrument
TOFRes_sample
TOFRes_monitor
Sample sends rays towards monitor.
Selects random final time in given interval.
Sample records q, E for each event
Monitor histograms those that reach it

## Slide 7: Resolution
  Terminal tool: mcresplot
Tools for detector response TOF case

## Slide 8: Resolution
  Separate for detector response and point spread function
    Point spread function can be determined for n spots at once with Spot_sample
  For detector response
    Existing solutions look at a single pixel (and time bin for TOF)
    Getting resolution function for whole detector requires
      Scan over instrument settings (incoming / final energy)
      Either scan over all pixel positions or large number of components
      For TOF instruments, scan over investigated time bin at given pixel
    These components are admittedly designed for TAS / simple TOF instruments
Current situation

## Slide 9: Resolution
  Want to get both detector response and point spread function
  Want to get entire detector and all times in one simulation
Method for full detector resolution
Start of instrument
Res_sample
Sample sends rays towards monitor.
Selects random final energy in given interval.
Monitor_nD
Monitor_nD
Monitor_nD
Before sample:
After sample:
Detector:
k, neutron id
k, neutron id
pixel position, time and neutron id

## Slide 10: Resolution
  For each event recorded in the detector we know
    From the detector itself: pixel position, time and neutron id
    From this id, we can look up: initial and final wavevector -> q, E
  With this information we can look at
    Small subset of pixel / time positions -> Detector response for that area in q, E
    Small subset of q, E -> Point spread function on detector
  This requires large dataset and code to handle data
  Still requires multiple simulations scanning over instrument settings
Method for full detector resolution